## Slide 1: An island energy system example
Annual electricity demand of the island: 250 kWyr
We want to plan the energy supply of an island, in order to meet its annual electricity demand
Source: Pexels.

## Slide 2
An island energy system example
The island has two power plants, one is based on coal, and other is based on natural gas.
How much should each power plant produce to meet the annual electricity demand of the island at minimum cost?
Plant | Production decision variable (kWyr) | Fuel requirement per unit production (kWyr/kWyr) | Cost of production (USD/kWyr) | Fuel availability (kWyr)
Coal PP | XCL | 3 | 350 | 600 (coal)
Gas PP | XGS | 2 | 300 | 300 (gas)
Notes: Let us collect the information we need to write the problem as a linear program:
Variables (which we must find the optimal value of): annual production of each power plant (Coal PP and Gas PP);
Objective function: minimize the annual production cost;
Constraints: max coal availability, max gas availability, min annual demand to be satisfied.

## Slide 3
Summary of data:
Annual electricity demand = 250 kWyr
Production costs:
Coal PP = 350 USD/kWyr
Gas PP = 300 USD/kWyr
Fuel requirement:
Coal PP = 3 kWyr/kWyr
Gas PP = 2 kWyr/kWyr
Fuel availability:
Coal = 600 kWyr
Gas = 300 kWyr
An island energy system example

## Slide 4
Formulation:
Minimize z = 350 * XCL + 300 * XGS
Subject to:
Production constraint: XCL + XGS ≥ 250
Coal availability constraint: 3* XCL ≤ 600
Gas availability constraint: 2* XGS ≤ 300
XCL ≥ 0, XGS ≥ 0
where XCL is the Coal PP production (kWyr)
XGS is the Gas PP production (kWyr)
An island energy system example
Notes: Let us collect the information we need to write the problem as a linear program:
Variables (which we must find the optimal value of): annual production of each power plant (Coal PP and Gas PP);
Objective function: minimize the annual production cost;
Constraints: min annual demand to be satisfied, max coal availability, max gas availability and of course non-negative values for the production of the two power plants.
From the information we collected, we can now write the formulation of the linear program.

## Slide 5
An island energy system example
Graphical representation of the constraints
XCL = Coal PP production (kWyr)
XGS = Gas PP production (kWyr)
Notes: Let us now represent how the constraints restrict the solution space.

## Slide 6
An island energy system example
Graphical representation of the constraints
XCL = Coal PP production (kWyr)
XGS = Gas PP production (kWyr)
1. Production constraint
Notes: First of all, the sum of the production of the coal and the gas power plant must be at least equal to 250 kWyr. This can be represented by the light blue line in the graph.

## Slide 7
An island energy system example
Graphical representation of the constraints
3* XCL ≤ 600
XCL = Coal PP production (kWyr)
XGS = Gas PP production (kWyr)
2. Coal availability constraint
Notes: Secondly, the use of coal must not exceed the coal availability, 600 kWyr. Since the use of coal is three times the production of the power plant, the production must not exceed 200 kWyr.

## Slide 8
An island energy system example
Graphical representation of the constraints
2* XGS ≤ 300
XCL = Coal PP production (kWyr)
XGS = Gas PP production (kWyr)
3. Gas availability constraint
Notes: A similar reasoning applier to the gas power plant. The use of gas must not exceed the gas availability, 300 kWyr. Since the use of gas is twice the production of the power plant, the production must not exceed 150 kWyr.

## Slide 9
An island energy system example
Graphical representation of the constraints
XCL = Coal PP production (kWyr)
XGS = Gas PP production (kWyr)
Solution space marked in dark red
Notes: Putting all the information together, we obtain the solution space, e.g. the area of the graph where the solution could lie. The solution will be a point in this area, determined by one value of production of the coal power plant XCL and one value of production of the gas power plant XGS.