## Slide 1: What is a Reference Energy System?
RES is a simplified and aggregated graphical representation of the real energy system under analysis;
RES covers not just the present configuration of the energy system, but also possible development paths;
It shows all existing and potential new energy supply chains, from primary energy resources to final demand;
The level of simplification depends on issues to be analysed and data availability;
RES should be a minimum representation of reality needed to answer the policy questions to be addressed;
Notes: We need to simplify and understand the representation of reality
And how if can evolve

## Slide 2: What is a Reference Energy System?
Extraction or Import
PRIMARY
SECONDARY
FINAL
USEFUL
Conversion
Conversion
Transmission & Distribution
Oil
Gas
Coal
water
Wind
Solar
- Diesel
Kerosene
Gas
Electricity
Coal
Heat
Lighting
Mechanical energy
Diesel
Kerosene
Gas
Electricity
Coal
An example: the electricity system

## Slide 3: What is a Reference Energy System?
RES consists of:
  Energy Levels
  Resources, Primary, Secondary,..., Final,…
    (extracted from resources, processed, converted, transmitted, distributed, …)
  Energy carriers / commodities
  Coal, oil, gas, wood, nuclear fuel, electricity, heat,…
  Technologies
  Which extract, process, convert energy from one to another form or to energy service, transmit and distribute

## Slide 4: What is a Reference Energy System?
Resources
Primary
Secondary
Final
Notes: Lines energy carriers: fuels/electricity
Boxes are the technologies

## Slide 5: How to design a RES?

## Slide 6: Where to start from: energy balance…
Notes: The energy balance is an accounting framework for compilation and reconciliation of data on all energy products entering, exiting and used within a country or area during a reference period (in this publication, a year).
Such a balance must necessarily express all forms of energy in a common accounting unit, and show the relationship between the inputs to and the outputs from the energy transformation processes.
Energy balances should be as complete as possible so that all energy flows are, in principle, accounted for.

## Slide 7: Where to start from: energy balance…
…
Commodities grouped into types
Notes: The energy balance is an accounting framework for compilation and reconciliation of data on all energy products entering, exiting and used within a country or area during a reference period (in this publication, a year).
Such a balance must necessarily express all forms of energy in a common accounting unit, and show the relationship between the inputs to and the outputs from the energy transformation processes.
Energy balances should be as complete as possible so that all energy flows are, in principle, accounted for.

## Slide 8: Where to start from: energy balance…
Primary production only
Notes: The energy balance is an accounting framework for compilation and reconciliation of data on all energy products entering, exiting and used within a country or area during a reference period (in this publication, a year).
Such a balance must necessarily express all forms of energy in a common accounting unit, and show the relationship between the inputs to and the outputs from the energy transformation processes.
Energy balances should be as complete as possible so that all energy flows are, in principle, accounted for.

## Slide 9: Where to start from: energy balance…
Secondary production reported here, together with energy converted (net value)
Notes: The energy balance is an accounting framework for compilation and reconciliation of data on all energy products entering, exiting and used within a country or area during a reference period (in this publication, a year).
Such a balance must necessarily express all forms of energy in a common accounting unit, and show the relationship between the inputs to and the outputs from the energy transformation processes.
Energy balances should be as complete as possible so that all energy flows are, in principle, accounted for.

## Slide 10: Where to start from: energy balance…
Negative: fuel burned to generate electricity
Notes: The energy balance is an accounting framework for compilation and reconciliation of data on all energy products entering, exiting and used within a country or area during a reference period (in this publication, a year).
Such a balance must necessarily express all forms of energy in a common accounting unit, and show the relationship between the inputs to and the outputs from the energy transformation processes.
Energy balances should be as complete as possible so that all energy flows are, in principle, accounted for.

## Slide 11: Where to start from: energy balance…
Positive: thermal electricity generated
Notes: The energy balance is an accounting framework for compilation and reconciliation of data on all energy products entering, exiting and used within a country or area during a reference period (in this publication, a year).
Such a balance must necessarily express all forms of energy in a common accounting unit, and show the relationship between the inputs to and the outputs from the energy transformation processes.
Energy balances should be as complete as possible so that all energy flows are, in principle, accounted for.

## Slide 12: Where to start from: energy balance…
Final consumption with break-down
Notes: The energy balance is an accounting framework for compilation and reconciliation of data on all energy products entering, exiting and used within a country or area during a reference period (in this publication, a year).
Such a balance must necessarily express all forms of energy in a common accounting unit, and show the relationship between the inputs to and the outputs from the energy transformation processes.
Energy balances should be as complete as possible so that all energy flows are, in principle, accounted for.

## Slide 13: Where to start from: energy balance…
Summary of all commodities – losses, efficiency can be assessed
Notes: The energy balance is an accounting framework for compilation and reconciliation of data on all energy products entering, exiting and used within a country or area during a reference period (in this publication, a year).
Such a balance must necessarily express all forms of energy in a common accounting unit, and show the relationship between the inputs to and the outputs from the energy transformation processes.
Energy balances should be as complete as possible so that all energy flows are, in principle, accounted for.

## Slide 14: Where to start from: energy balance…
https://unstats.un.org/unsd/energy/balance/default.htm

## Slide 15: Where to start from: energy flows…
https://www.iea.org/Sankey/

## Slide 16: Where to start from…
The energy balance (or, if available, the energy flows) can be used as a starting point for drawing a RES. The main steps to be taken are:
  Identification of energy levels and energy carriers;
  Identification of technologies.

## Slide 17: 1. Identification of energy levels and carriers
1
2
3
4
5

## Slide 18: 1. Identification of energy levels and carriers
1
2
3
4
5
Resources
Primary
Secondary
Final

## Slide 19: 2. Identification of technologies
Which energy conversion technologies are currently used to transform primary energy to final energy in every level and/or are planned for the future?
Which energy transmission/transportation technologies are currently used and/or are planned for the future?
Make list of technologies and group those that share similar characteristics

## Slide 20: 3. Simplify and aggregate:
A real electricity system might look something like this:

## Slide 21: 3. Simplify and aggregate:
All technologies of similar kind aggregated together and only fundamental links between them captured.
Production
Transmission
Distribution
Consumption
Transmission/
distribution

## Slide 22: 4. Represent the main inputs and outputs:

## Slide 23: 4. Represent the main inputs and outputs:
Refinery
Crude oil
LPG
Gasoline
Kerosene
Diesel
HFO
Input
Output
Motor fuels

## Slide 24: Regionalisation

## Slide 25: Regionalisation
The energy systems of different neighbouring regions can be represented by as many Reference Energy Systems (RES).
These will be linked by import/export technologies.