## Slide 1: Scenario types and techniques
Let us try and sort the scenarios of Lab 5 in these 3 categories...

## Slide 2
In the base case (which we will call Business As Usual – BAU – scenario), the availability of wind was considered constant throughout the seasons and across day and night.
By better observation of historical data for the location of wind farms in Simplicity, researchers have noticed that there actually is a difference of wind availability across seasons and between day and night. This reflects in different capacity factors for wind technologies. In summer time, capacity factors are as low as 12% during the night and 5% during the day. In the intermediate season, they are 10% and 20% in the night and day, respectively. In winter time, they become as high as 30% during the night and 15% during the day.
Scenario 1: reduced wind availability

## Slide 3
In the base case (which we will call Business As Usual – BAU – scenario), the availability of wind was considered constant throughout the seasons and across day and night.
By better observation of historical data for the location of wind farms in Simplicity, researchers have noticed that there actually is a difference of wind availability across seasons and between day and night. This reflects in different capacity factors for wind technologies. In summer time, capacity factors are as low as 12% during the night and 5% during the day. In the intermediate season, they are 10% and 20% in the night and day, respectively. In winter time, they become as high as 30% during the night and 15% during the day.
Predictive
Scenario 1: reduced wind availability

## Slide 4
Huge investments in the production of solar PV technologies in China and India and new trade agreements with Simplicity result in an abrupt decrease of the technology supply price from 2023 on. The capital cost of solar PV panels without storage becomes 1100 $/kW in 2023 and then linearly decreases down to 800 $/kW in 2040. The capital cost of PV panels including storage becomes 1800 $/kW in 2023 and decreases to 1200 $/kW in 2040.
Additionally, technological advancements make so that the capacity factors of solar PV in day time increase significantly, to 40% regardless the season.
Scenario 2: breakthrough in solar technologies

## Slide 5
Huge investments in the production of solar PV technologies in China and India and new trade agreements with Simplicity result in an abrupt decrease of the technology supply price from 2023 on. The capital cost of solar PV panels without storage becomes 1100 $/kW in 2023 and then linearly decreases down to 800 $/kW in 2040. The capital cost of PV panels including storage becomes 1800 $/kW in 2023 and decreases to 1200 $/kW in 2040.
Additionally, technological advancements make so that the capacity factors of solar PV in day time increase significantly, to 40% regardless the season.
Explorative
Scenario 2: breakthrough in solar technologies

## Slide 6
The Government of Simplicity decides to pursue sustainability goals for the energy sector primarily through demand-side measures. A target of 5% annual energy savings in final uses for users already connected to the network is imposed from 2022 to 2025. After that, it is increased to 7.5% up to 2030. It becomes 10% thereafter.
Scenario 3: Energy Efficiency targets

## Slide 7
The Government of Simplicity decides to pursue sustainability goals for the energy sector primarily through demand-side measures. A target of 5% annual energy savings in final uses for users already connected to the network is imposed from 2022 to 2025. After that, it is increased to 7.5% up to 2030. It becomes 10% thereafter.
Normative
Scenario 3: Energy Efficiency targets

## Slide 8
Simplicity has large biomass resources, coming primarily from forestry residues. The state-owned utility decides to evaluate the possibility of using biomass to meet part of the heating and electricity demand in the residential sector, through Combined Heat & Power (CHP) plants, starting 2023. The CHP plants shall be connected to the Transmission Grid.
The biomass would have a cost of 1.5 $/GJ.
The new CHP plants would have to meet an annual heat demand growing linearly from 0.4 PJ in 2023 to 1 PJ in 2040. The demand has a flat profile across seasons and day parts.
Scenario 4: heat and electricity from biomass

## Slide 9
Simplicity has large biomass resources, coming primarily from forestry residues. The state-owned utility decides to evaluate the possibility of using biomass to meet part of the heating and electricity demand in the residential sector, through Combined Heat & Power (CHP) plants, starting 2023. The CHP plants shall be connected to the Transmission Grid.
The biomass would have a cost of 1.5 $/GJ.
The new CHP plants would have to meet an annual heat demand growing linearly from 0.4 PJ in 2023 to 1 PJ in 2040. The demand has a flat profile across seasons and day parts.
Explorative
Scenario 4: heat and electricity from biomass

## Slide 10
The Government of Simplicity decides to support the generation by solar power plants by imposing a target of generation by PV power plants (either with or without storage). The target increases from 5% of the final electricity supply for new connections in 2020 to 70% in 2040.
Scenario 5: solar generation target

## Slide 11
The Government of Simplicity decides to support the generation by solar power plants by imposing a target of generation by PV power plants (either with or without storage). The target increases from 5% of the final electricity supply for new connections in 2020 to 70% in 2040.
Normative
Scenario 5: solar generation target

## Slide 12
By taking a close look at long-term historical data series of water flow in rivers across seasons, researchers find out that the flow is being significantly affected by climatic change. The Government acts right away by imposing that hydropower generation be reduced consequently from 2020 on, in order not to further affect the water ecosystem and not to reduce the availability of water for agricultural uses.
In summer, the maximum capacity factors of run of river power plants are reduced to 20%; in winter, to 30%; in the intermediate season, to 25%. The capacity of the River feeding the dam hydro power plants, instead, reduces to 30% in summer, 35% in the intermediate season and 40% in winter.
Scenario 6: Climate change

## Slide 13
By taking a close look at long-term historical data series of water flow in rivers across seasons, researchers find out that the water flow is being significantly affected by climatic change. The Government acts right away by imposing that hydropower generation be reduced consequently from 2020 on, in order not to further affect the water ecosystem and not to reduce the availability of water for agricultural uses.
In summer, the maximum capacity factors of run of river power plants are reduced to 20%; in winter, to 30%; in the intermediate season, to 25%. The capacity of the River feeding the dam hydro power plants, instead, reduces to 30% in summer, 35% in the intermediate season and 40% in winter.
Normative
Scenario 6: Climate change

## Slide 14
The plan presented in Scenario 6 does not work as expected. Investors are not able to invest quickly enough to replace the missing hydro generation. While the capacity factors reduce exactly like in the previous case, the total capacity of all power plant types does not change as compared to what OBTAINED from Scenario 1 (hint: constrain all capacities of power plants for all years to values of capacity obtained as results in Scenario 1).
Investigate whether it is still possible to meet the electricity demand in these conditions.
Scenario 7: Climate change with no adaptation

## Slide 15
The plan presented in Scenario 6 does not work as expected. Investors are not able to invest quickly enough to replace the missing hydro generation. While the capacity factors reduce exactly like in the previous case, the total capacity of all power plant types does not change as compared to what OBTAINED from Scenario 1 (hint: constrain all capacities of power plants for all years to values of capacity obtained as results in Scenario 1).
Investigate whether it is still possible to meet the electricity demand in these conditions.
Explorative
Scenario 7: Climate change with no adaptation

## Slide 16
Scenario 8: Climate change with no adaptation – import potential
A contingency plan to build a line for electricity import from a neighbouring country (operational from 2028) may reduce the stress caused in the previous scenario. The cost of imported electricity is expected to be constant and equal to 0.1 $/kWh. The investment costs are considered sunk costs in this situation and can be disregarded.

## Slide 17
Scenario 8: Climate change with no adaptation – import potential
A contingency plan to build a line for electricity import from a neighbouring country (operational from 2028) may reduce the stress caused in the previous scenario. The cost of imported electricity is expected to be constant and equal to 0.1 $/kWh. The investment costs are considered sunk costs in this situation and can be disregarded.
Explorative

## Slide 18
Until 2025, in Simplicity all transportation feeds on fossil fuels. From 2025, however, the population starts becoming aware of the huge environmental impacts on fossil-fuel-fired transportation. This, combined with a strong decrease in the prices of electric vehicles, due to economies of scale in other countries, and with infrastructure investments by the Government, causes a new demand for electricity for EVs to arise gradually. Such demand is null in 2025 and becomes comparable to the sum of all other electricity demands in 2040.
This demand has a different profile from the one for electricity for other uses: the profile of the demand is flat across seasons, but 75% of it happens during the night (as the vehicles are connected to the network and recharged during the night).
The vechicles will feed on the grid for existing users, but it is expected that more investments in power generation will be needed to meet this demand.
Scenario 9: Electrification of transport

## Slide 19
Until 2025, in Simplicity all transportation feeds on fossil fuels. From 2025, however, the population starts becoming aware of the huge environmental impacts on fossil-fuel-fired transportation. This, combined with a strong decrease in the prices of electric vehicles, due to economies of scale in other countries, and with infrastructure investments by the Government, causes a new demand for electricity for EVs to arise gradually. Such demand is null in 2025 and becomes comparable to the sum of all other electricity demands in 2040.
This demand has a different profile from the one for electricity for other uses: the profile of the demand is flat across seasons, but 75% of it happens during the night (as the vehicles are connected to the network and recharged during the night).
The vechicles will feed on the grid for existing users, but it is expected that more investments in power generation will be needed to meet this demand.
Explorative
Scenario 9: Electrification of transport

## Slide 20
Think of a movie where something happens which causes huge, disruptive changes in energy supply and/or demand, create a short story for it (like the ones of all previous slides) and model it.
Think about whether your movie scenario is predictive, explorative or normative...
Scenario 10: Movie scenario