## Slide 1: List of parameters, default values and units
Here you find a summary of all the input parameters of OSeMOSYS.
It includes:
Name in OSeMOSYS (also displayed in MoManI);
Short description (also displayed in MoManI);
Suggested Default value: this value is assigned to the parameter whenever you do not assign a value yourself. It is therefore of extreme importance. Many times models are not feasible because we forgot to assign an appropriate Default value. In MoManI, Default values are already assigned, but sometimes they may be wrong, for some reason. Alsways cross-check the values with those suggested here;
Default unit.
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 2: List of parameters, default values and units
Name | Description | Default value | Unit
AccumulatedAnnualDemand | Accumulated Demand for a certain commodity in one specific year. It cannot be defined for a commodity if its SpecifiedAnnualDemand for the same year is already defined and vice versa. | 0 | PJ
AnnualEmissionLimit | Annual upper limit for a specific emission generated in the whole modelled region. | 99999 | Mton
AnnualExogenousEmission | It allows the user to account for additional annual emissions, on top of those computed endogenously by the model (e.g. emissions generated outside the region). | 0 | Mton
AvailabilityFactor | Capacity available on average over one year, expressed as a fraction of the total installed capacity. Value ranging from 0 to 1. It gives the possibility to account for planned outages. | 1 | -
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 3: List of parameters, default values and units
Name | Description | Default value | Unit
CapacityFactor | Capacity available on average over every time slice, expressed as a fraction of the total installed capacity. Value ranging from 0 to 1. It gives the possibility to account for unplanned outages. | 1 | -
CapacityOfOneTechnologyUnit | Capacity of one new unit of a technology. In case the user sets this parameter, the related technology will be installed only in batches of the specified capacity and the problem will turn into a Mixed Integer Linear Problem. | 0 | GW
CapacityToActivityUnit | Conversion factor relating the energy that would be produced when one unit of capacity is fully used in one year. | 1 | PJ/GW
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 4: List of parameters, default values and units
Name | Description | Default value | Unit
CapitalCost | Capital investment cost of a technology, per unit of capacity. | 0.0001 | M$/GW
CapitalCostStorage | Binary parameter linking a technology to the storage facility it charges. It has value 0 if the technology and the storage facility are not linked, 1 if they are. | 0.0001 | M$/PJ
Conversionld | Binary parameter linking one TimeSlice to a certain DayType. It has value 0 if the TimeSlice does not pertain to the specific DayType, 1 if it does. | 0 | -
Conversionlh | Binary parameter linking one TimeSlice to a certain DaylyTimeBracket. It has value 0 if the TimeSlice does not pertain to the specific DaylyTimeBracket, 1 if it does. | 0 | -
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 5: List of parameters, default values and units
Name | Description | Default value | Unit
Conversionls | Binary parameter linking one TimeSlice to a certain Season. It has value 0 if the TimeSlice does not pertain to the specific season, 1 if it does. | 0 | -
DaysInDayType | Number of days for each day type, within one week (natural number, ranging from 1 to 7) | 7 | -
DaySplit | Length of one DailyTimeBracket in one specific day as a fraction of the year (e.g., when distinguishing between days and night: 12h/(24h*365d)). | 0.00137 | -
DepreciationMethod | Binary parameter defining the type of depreciation to be applied. It has value 1 for sinking fund depreciation, value 2 for straight-line depreciation. | 1 | -
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 6: List of parameters, default values and units
Name | Description | Default value | Unit
DiscountRate | Region-specific value for the discount rate, expressed in decimals (e.g. 0.05) | 0.05 | -
EmissionActivityRatio | Emission factor of a technology per unit of activity, per mode of operation. | 0 | Mt/PJ
EmissionsPenalty | Taxation per unit of emission. | - | M$/Mt
FixedCost | Fixed O&M cost of a technology, per unit of capacity. | 0.0001 | M$/GW
InputActivityRatio | Rate of input (use) of a fuel (commodity) by a technology, as a ratio of the rate of activity. | 0 | -
MinStorageCharge | It sets a lower bound to the amount of energy stored, as a fraction of the maximum, with a number ranging between 0 and 1. The storage facility cannot be emptied below this level. | 0 | PJ
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 7: List of parameters, default values and units
Name | Description | Default value | Unit
ModelPeriodEmissionLimit | Annual upper limit for a specific emission generated in the whole modelled region, over the entire modelled period. | 999999 | Mt
ModelPeriodExogenousEmission | It allows the user to account for additional emissions over the entire modelled period, on top of those computed endogenously by the model (e.g. generated outside the region). | 0 | Mt
OperationalLife | Useful lifetime of a technology, expressed in years. | 1 | Years
OperationalLifeStorage | The useful lifetime of the storage facility. | 1 | Years
OutputActivityRatio | The rate of output of fuel (commodity) as a ratio to the rate of activity in which a technology is operating. | 0 | -
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 8: List of parameters, default values and units
Name | Description | Default value | Unit
REMinProductionTarget | Minimum ratio of all renewable commodities tagged in the RETagCommodity parameter, to be produced by the technologies tagged with the RETechnology parameter. | 0 | -
ReserveMargin | Minimum level of the reserve margin required to be provided for all the tagged commodities, by the tagged technologies. If no reserve margin is required, the parameter will have value 1; if, for instance, 20% reserve margin is required, the parameter will have value 1.2. | 1 | -
ReserveMarginTagFuel | Binary parameter tagging the fuels to which the reserve margin applies. It has value 1 if the reserve margin applies to the fuel, 0 otherwise. | 0 | -
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 9: List of parameters, default values and units
Name | Description | Default value | Unit
ReserveMarginTagTechnology | Binary parameter tagging the technologies that are allowed to contribute to the reserve margin. It has value 1 for the technologies allowed, 0 otherwise. | 0 | -
ResidualCapacity | Capacity left over from a period prior to the modelling period. | 0 | GW
ResidualStorageCapacity | Storage capacity left over from a period prior to the modelling period. | 0 | PJ
RETagFuel | Binary parameter tagging the fuels to which the renewable target applies to. It has value 1 if the target applies, 0 otherwise. | 0 | -
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 10: List of parameters, default values and units
Name | Description | Default value | Unit
RETagTechnology | Binary parameter tagging the renewable technologies that must contribute to reaching the indicated minimum renewable production target. It has value 1 for the technologies contributing, 0 otherwise. | 0 | -
SpecifiedAnnualDemand | Total specified demand for the year, linked to a specific ‘time of use’ during the year. | 0 | PJ
SpecifiedDemandProfile | Annual fraction of energy-service or commodity demand that is required in each time slice. For each year, all the defined SpecifiedDemandProfile input values should sum up to 1. | 0 | -
StorageLevelStart | Level of storage at the beginning of first modelled year, in units of activity. | 0 | PJ
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 11: List of parameters, default values and units
Name | Description | Default value | Unit
StorageMaxChargeRate | Maximum charging rate for the storage, in units of activity per year. | 99999 | PJ
StorageMaxDischargeRate | Maximum discharging rate for the storage, in units of activity per year. | 99999 | PJ
TechnologyFromStorage | Binary parameter linking a storage facility to the technology it feeds. It has value 1 if the technology and the storage facility are linked, 0 otherwise. | 0 | -
TechnologyToStorage | Binary parameter linking a technology to the storage facility it charges. It has value 1 if the technology and the storage facility are linked, 0 otherwise. | 0 | -
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 12: List of parameters, default values and units
Name | Description | Default value | Unit
TotalAnnualMaxCapacity | Total maximum existing (residual plus cumulatively installed) capacity allowed for a technology in a specified year. | 999999 | GW
TotalAnnualMaxCapacityInvestment | Maximum capacity of a technology expressed in power units. | 999999 | GW
TotalAnnualMinCapacity | Total minimum existing (residual plus cumulatively installed) capacity allowed for a technology in a specified year. | 0 | GW
TotalAnnualMinCapacityInvestment | Minimum capacity of a technology expressed in power units. | 0 | GW
TotalTechnologyAnnualActivityLowerLimit | Total minimum level of activity allowed for a technology in one year. | 0 | PJ
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 13: List of parameters, default values and units
Name | Description | Default value | Unit
TotalTechnologyAnnualActivityUpperLimit | Total maximum level of activity allowed for a technology in one year. | 9999999 | PJ
TotalTechnologyModelPeriodActivityLowerLimit | Total minimum level of activity allowed for a technology in the entire modelled period. | 0 | PJ
TotalTechnologyModelPeriodActivityUpperLimit | Total maximum level of activity allowed for a technology in the entire modelled period. | 9999999 | PJ
TradeRoute | Binary parameter defining the links between region r and region rr, to enable or disable trading of a specific commodity. It has value 1 when two regions are linked, 0 otherwise | 0 | -
VariableCost | Cost of a technology for a given mode of operation (Variable O&M cost), per unit of activity. | 0.0001 | M$/PJ
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.

## Slide 14: List of parameters, default values and units
Name | Description | Default value | Unit
YearSplit | Duration of a modelled time slice expressed as a fraction of the year. The sum of each entry over one modelled year should equal 1. | 0 | -
Notes: GNU MathProg is one of the simplest modelling languages. It is open-source and similar to GAMS. Equations written in GNU MathProg resemble equations written in the algebraic form, such as those one could write manually on paper.